NEOS-MOUSE DRIVER
-----------------


  This little code example shows how to use the neos-mouse into a program.
Neos-mouse has two modes, one of them is the joystick mode. If you plug the 
mouse while the left button is depressed, it behaves as a joystick. If you just
plug it without pressing any of its buttons, neos-mouse will be in the native
mode. This mode is far different from the mouse mode of the 1351 mouse. It sends
its data in four parts, which are the nibbles of the direction information.
It uses the paddle byte one of the SID for representing the right button. Left
button corresponds to the fire button of a joystick.

   The code is loaded into $c000-$c1f8 area. You can execute it by loading 
it like load'neos-driver',8,1 and typing sys49152. You should be able to move 
the pointer with a neos-mouse plugged into the joystick port-1. If you press 
left key you can terminate the program. But, as you know you cannot use the
keyboard when this mouse is plugged. So, you have to unplug it when you need 
to type something.
 
   The code at the $c100 reads the mouse, $c190 converts direction bytes into 
the screen coordinates, and $c1d0 moves the pointer. Sprite of the pointer is
transfered to the location begining from $0340.

   I hope this little document is enough for exploring the neos-driver code.



Ilker Ficicilar
filker@newton.physics.metu.edu.tr
e068214@orca.cc.metu.edu.tr


---